## Slide 1: Multimedia Applications
Multimedia requirements
Streaming
Phone over IP
Recovering from Jitter and Loss
RTP
Diff-serv, Int-serv, RSVP

## Slide 2: Application Classes
Typically sensitive to delay, but can tolerate packet loss (would cause minor glitches that can be concealed)
Data contains audio and video content (“continuous media”), three classes of applications:
  Streaming
  Unidirectional Real-Time
  Interactive Real-Time

## Slide 3: Application Classes (more)
Streaming
  Clients request audio/video files from servers and pipeline reception over the network and display
  Interactive: user can control operation (similar to VCR: pause, resume, fast forward, rewind, etc.)
  Delay: from client request until display start can be 1 to 10 seconds

## Slide 4: Application Classes (more)
Unidirectional Real-Time:
  similar to existing TV and radio stations, but delivery on the network
  Non-interactive, just listen/view
Interactive Real-Time :
  Phone conversation or video conference
  More stringent delay requirement than Streaming and Unidirectional because of real-time nature
  Video: < 150 msec acceptable
  Audio: < 150 msec good, <400 msec acceptable

## Slide 5: Challenges
TCP/UDP/IP suite provides best-effort, no guarantees on expectation or variance of packet delay
Streaming applications delay of 5 to 10 seconds is typical and has been acceptable, but performance deteriorate if links are congested (transoceanic)
Real-Time Interactive requirements on delay and its jitter have been satisfied by over-provisioning (providing plenty of bandwidth), what will happen when the load increases?...

## Slide 6: Challenges (more)
Most router implementations use only First-Come-First-Serve (FCFS) packet processing and transmission scheduling
To mitigate impact of “best-effort” protocols, we can:
  Use UDP to avoid TCP and its slow-start phase…
  Buffer content at client and control playback to remedy jitter
  Adapt compression level to available bandwidth

## Slide 7: Solution Approaches in IP Networks
Just add more bandwidth and enhance caching capabilities (over-provisioning)!
Need major change of the protocols :
  Incorporate resource reservation (bandwidth, processing, buffering), and new scheduling policies
  Set up service level agreements with applications, monitor and enforce the agreements, charge accordingly
Need moderate changes (“Differentiated Services”):
  Use two traffic classes for all packets and differentiate service accordingly
  Charge based on class of packets
  Network capacity is provided to ensure first class packets incur no significant delay at routers

## Slide 8: Streaming
Important and growing application due to reduction of storage costs, increase in high speed net access from homes, enhancements to caching and introduction of QoS in IP networks
Audio/Video file is segmented and sent over either TCP or UDP, public segmentation protocol: Real-Time Protocol (RTP)

## Slide 9: Streaming
User interactive control is provided, e.g. the public protocol Real Time Streaming Protocol (RTSP)
Helper Application: displays content, which is typically requested via a Web browser; e.g. RealPlayer; typical functions:
  Decompression
  Jitter removal
  Error correction: use redundant packets to be used for reconstruction of original stream
  GUI for user control

## Slide 10: Streaming From Web Servers
Audio: in files sent as HTTP objects
Video (interleaved audio and images in one file, or two separate files and client synchronizes the display) sent as HTTP object(s)
A simple architecture is to have the Browser requests the object(s) and after their reception pass them to the player for display
  - No pipelining

## Slide 11: Streaming From Web Server (more)
Alternative: set up connection between server and player, then download
Web browser requests and receives a Meta File (a file describing the object) instead of receiving the file itself;
Browser launches the appropriate Player and passes it the Meta File;
Player sets up a TCP connection with Web Server and downloads the file

## Slide 12: Meta file requests

## Slide 13: Using a Streaming Server
This gets us around HTTP, allows a choice of UDP vs. TCP and the application layer protocol can be better tailored to Streaming; many enhancements options are possible (see next slide)

## Slide 14: Options When Using a Streaming Server
Use UDP, and Server sends at a rate (Compression and Transmission) appropriate for client; to reduce jitter, Player buffers initially for 2-5 seconds, then starts display
Use TCP, and sender sends at maximum possible rate under TCP; retransmit when error is encountered; Player uses a much large buffer to smooth delivery rate of TCP

## Slide 15: Real Time Streaming Protocol (RTSP)
For user to control display: rewind, fast forward, pause, resume, etc…
Out-of-band protocol (uses two connections, one for control messages (Port 554) and for media stream)
RFC 2326 permits use of either TCP or UDP for the control messages connection, sometimes called the RTSP Channel
As before, meta file is communicated to web browser which then launches the Player; Player sets up an RTSP connection for control messages in addition to the connection for the streaming media

## Slide 16: Meta File Example
<title>Twister</title>
<session>
<group language=en lipsync>
<switch>
<track type=audio
e="PCMU/8000/1"
src = "rtsp://audio.example.com/twister/audio.en/lofi">
<track type=audio
e="DVI4/16000/2" pt="90 DVI4/8000/1"
src="rtsp://audio.example.com/twister/audio.en/hifi">
</switch>
<track type="video/jpeg"
src="rtsp://video.example.com/twister/video">
</group>
</session>

## Slide 17: RTSP Operation

## Slide 18: RTSP Exchange Example
C: SETUP rtsp://audio.example.com/twister/audio RTSP/1.0
Transport: rtp/udp; compression; port=3056; mode=PLAY
S: RTSP/1.0 200 1 OK
Session 4231
C: PLAY rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=0-
C: PAUSE rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=37
C: TEARDOWN rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
S: 200 3 OK

## Slide 19: Real-Time (Phone) Over IP’s Best-Effort
Internet phone applications generate packets during talk spurts
Bit rate is 8 KBytes, and every 20 msec, the sender forms a packet of 160 Bytes + a header to be discussed below
The coded voice information is encapsulated into a UDP packet and sent out; some packets may be lost; up to 20 % loss is tolerable; using TCP eliminates loss but at a considerable cost: variance in delay; FEC is sometimes used to fix errors and make up losses

## Slide 20: Real-Time (Phone) Over IP’s Best-Effort
End-to-end delays above 400 msec cannot be tolerated; packets that are that delayed are ignored at the receiver
Delay jitter is handled by using timestamps, sequence numbers, and delaying playout at receivers either a fixed or a variable amount
With fixed playout delay, the delay should be as small as possible without missing too many packets; delay cannot exceed 400 msec

## Slide 21: Internet Phone with Fixed Playout Delay

## Slide 22: Adaptive Playout Delay
Objective is to use a value for p-r that tracks the network delay performance as it varies during a phone call
The playout delay is computed for each talk spurt based on observed average delay and observed deviation from this average delay
Estimated average delay and deviation of average delay are computed in a manner similar to estimates of RTT and deviation in TCP
The beginning of a talk spurt is identified from examining the timestamps in successive and/or sequence numbers of chunks

## Slide 23: Recovery From Packet Loss
Loss is in a broader sense: packet never arrives or arrives later than its scheduled playout time
Since retransmission is inappropriate for Real Time applications, FEC or Interleaving are used to reduce loss impact.
FEC is Forward Error Correction
Simplest FEC scheme adds a redundant chunk made up of exclusive OR of a group of n chunks; redundancy is 1/n; can reconstruct if at most one lost chunk; playout time schedule assumes a loss per group

## Slide 24: Recovery From Packet Loss
Mixed quality streams are used to include redundant duplicates of chunks; upon loss playout available redundant chunk, albeit a lower quality one
With one redundant chunk per chunk can recover from single losses

## Slide 25: Piggybacking Lower Quality Stream

## Slide 26: Interleaving
Has no redundancy, but can cause delay in playout beyond Real Time requirements
Divide 20 msec of audio data into smaller units of 5 msec each and interleave
Upon loss, have a set of partially filled chunks