## Slide 1: Chapter 14 MPEG Audio Compression
14.1 Psychoacoustics
14.2 MPEG Audio
14.3 Other Audio Codecs
14.4 MPEG-7 Audio and Beyond

## Slide 2: 14.1 Psychoacoustics
The range of human hearing is about 20 Hz to about 20 kHz.
The frequency range of the voice is typically only from about 500 Hz to 4 kHz.
The dynamic range, the ratio of the maximum sound amplitude to the quietest sound that humans can hear, is on the order of about 120 dB.

## Slide 3: Equal-Loudness Relations
Fletcher-Munson Curves
  Equal loudness curves that display the relationship between perceived loudness (“Phons”, in dB) for a given stimulus sound volume (“Sound Pressure Level”, also in dB), as a function of frequency.
Fig. 14.1 shows the ear’s perception of equal loudness:
  The bottom curve, for example, shows what level of pure tone stimulus is required to produce the perception of a 10 dB sound.
  All the curves are arranged so that the perceived loudness level gives the same loudness as for that loudness level of a pure tone at 1 kHz.

## Slide 4
Fig. 14.1: Fletcher-Munson Curves (re-measured by Robinson and Dadson)

## Slide 5: Frequency Masking
Lossy audio data compression methods, such as MPEG/Audio encoding, remove some sounds which are masked anyway.
The general situation in regard to masking is as follows:
  A lower tone can effectively mask (make us unable to hear) a higher tone.
  The reverse is not true – a higher tone does not mask a lower tone well.
  The greater the power in the masking tone, the wider is its influence – the broader the range of frequencies it can mask.
  As a consequence, if two tones are widely separated in frequency then little masking occurs.

## Slide 6: Threshold of Hearing
A plot of the threshold of human hearing for a pure tone
Fig. 14.2: Threshold of human hearing, for pure tones

## Slide 7: Threshold of Hearing (Cont’d)
The threshold of hearing curve: if a sound is above the dB level shown then the sound is audible.
Turning up a tone so that it equals or surpasses the curve means that we can then distinguish the sound.
An approximate formula exists for this curve:
(14.1)
The threshold units are dB; the frequency for the origin
(0,0) in formula (14.1) is 2,000 Hz: Threshold(f) = 0 at f =2 kHz.

## Slide 8: Frequency Masking Curves
Frequency masking is studied by playing a particular pure tone, say 1 kHz, at a loud volume, and determining how this tone affects our ability to hear tones nearby in frequency.
  One would generate a 1 kHz masking tone, at a fixed sound level of 60 dB, and then raise the level of a nearby tone, e.g., 1.1 kHz, until it is just audible.
The threshold in Fig. 14.3 plots the audible level for a single masking tone (1 kHz).
Fig. 14.4 shows how the plot changes if other masking tones are used.

## Slide 9
Fig. 14.3: Effect on threshold for 1 kHz masking tone

## Slide 10
Fig. 14.4: Effect of masking tone at three different frequencies

## Slide 11: Critical Bands
Critical bandwidth represents the ear’s resolving power for simultaneous tones or partials.
  At the low-frequency end, a critical band is less than 100 Hz wide, while for high frequencies the width can be greater than 4 kHz.
Experiments indicate that the critical bandwidth:
  for masking frequencies < 500Hz: remains approximately constant in width ( about 100 Hz)
  For masking frequencies > 500Hz: increases approximately linearly with frequency.

## Slide 12: Table 14.1: 25 Critical Bands and Their Bandwidths

## Slide 14: Bark Unit
Bark unit is defined as the width of one critical band, for any masking frequency.
The idea of the Bark unit: every critical band width is roughly equal in terms of Barks (refer to Fig. 14.5).
Fig. 14.5: Effect of masking tones, expressed in Bark units

## Slide 15: Conversion: Frequency & Critical Band Number
• Conversion expressed in the Bark unit:
(14.2)
• Another formula used for the Bark scale:
(14.3)
where f is in kHz and b is in Barks (the same applies to all below).
The inverse equation:
(14.4)
The critical bandwidth (df) for a given center frequency f can also be approximated by:
(14.5)

## Slide 16: Temporal Masking
Phenomenon: any loud tone will cause the hearing receptors in the inner ear to become saturated and require time to recover
The following figures show the results of masking experiments:

## Slide 17
Fig.14.6: The louder the test tone, the shorter the amount of time required before the test tone is audible once the masking tone is removed.

## Slide 18
Fig. 14.7: Effect of temporal masking depends on both time and closeness in frequency.

## Slide 19
Fig.14.8: For a masking tone that is played for a longer time, it takes longer before a test tone can be heard. Solid curve: masking tone played for 200 msec; dashed curve: masking tone played for 100 msec.

## Slide 20: 14.2 MPEG Audio
MPEG audio compression takes advantage of psychoacoustic models, constructing a large multi-dimensional lookup table to transmit masked frequency components using fewer bits.
MPEG Audio Overview
  Applies a filter bank to the input to break it into its frequency components.
  In parallel, a psychoacoustic model is applied to the data for bit allocation block.
  The number of bits allocated are used to quantize the info from the filter bank – providing the compression.

## Slide 21: MPEG Layers
MPEG audio offers three compatible layers:
  Each succeeding layer able to understand the lower layers.
  Each succeeding layer offering more complexity in the psychoacoustic model and better compression for a given level of audio quality.
  each succeeding layer, with increased compression effectiveness, accompanied by extra delay.
The objective of MPEG layers: a good tradeoff between quality and bitrate.

## Slide 22: MPEG Layers (Cont’d)
Layer 1 quality can be quite good provided a comparatively high bitrate is available.
  Digital Audio Tape typically uses Layer 1 at around 192 kbps.
Layer 2 has more complexity; was proposed for use in Digital Audio Broadcasting.
Layer 3 (MP3) is most complex, and was originally aimed at audio transmission over ISDN lines.
Most of the complexity increase is at the encoder, not the decoder – accounting for the popularity of MP3 players.

## Slide 23: MPEG Audio Strategy
• MPEG approach to compression relies on:
  Quantization
  Inaccuracy of human auditory system within the width of a critical band.
• MPEG encoder employs a bank of filters to:
  Analyze the frequency (“spectral”) components of the audio signal by calculating a frequency transform of a window of signal values.
  Decompose the signal into subbands by using a bank of filters (Layer 1 & 2: “quadrature-mirror”; Layer 3: adds a DCT; psychoacoustic model: Fourier transform).

## Slide 24: MPEG Audio Strategy (Cont’d)
Frequency masking: by using a psychoacoustic model to estimate the just noticeable noise level:
  Encoder balances the masking behavior and the available number of bits by discarding inaudible frequencies.
  Scaling quantization according to the sound level that is left over, above masking levels.
May take into account the actual width of the critical bands:
  As mentioned earlier, audible frequencies are usually divided into 25 main critical bands (Table 14.1).
  To keep simplicity, the MPEG model adopts a uniform width for all frequency analysis filters, using 32 overlapping subbands.

## Slide 25: MPEG Audio Compression Algorithm
Fig. 14.9: Basic MPEG Audio encoder and decoder.

## Slide 26: Basic Algorithm (Cont’d)
The algorithm proceeds by dividing the input into 32 frequency subbands, via a filter bank.
  A linear operation taking 32 PCM samples, sampled in time; output is 32 frequency coefficients.
In the Layer 1 encoder, the sets of 32 PCM values are first assembled into a set of 12 groups of 32s.
  an inherent time lag in the coder, equal to the time to accumulate 384 (i.e., 12×32) samples.
Fig.14.11 shows how samples are organized.
  A Layer 2 or Layer 3 frame actually accumulates more than 12 samples for each subband: a frame includes 1,152 samples.

## Slide 27
Fig. 14.11: MPEG Audio Frame Sizes

## Slide 28: Bit Allocation Algorithm
Aim: ensure that all of the quantization noise is below the masking thresholds.
One common scheme:
  For each subband, the psychoacoustic model calculates the Signal-to-Mask Ratio (SMR) in dB.
  Then the “Mask-to-Noise Ratio” (MNR) is defined as the difference (as shown in Fig.14.12):
  (14.7)
  The lowest MNR is determined, and the number of code-bits allocated to this subband is incremented.
  Then a new estimate of the SNR is made, and the process iterates until there are no more bits to allocate.

## Slide 29
Fig. 14.12: MNR and SMR. A qualitative view of SNR, SMR and MNR are shown, with one dominate masker and m bits allocated to a particular critical band.

## Slide 30
• Mask calculations are performed in parallel with subband filtering, as in Fig. 4.13:
Fig. 14.13: MPEG-1 Audio Layers 1 and 2.

## Slide 31: Layer 2 of MPEG-1 Audio
• Main difference:
  Three groups of 12 samples are encoded in each frame and temporal masking is brought into play, as well as frequency masking.
  Bit allocation is applied to window lengths of 36 samples instead of 12.
  The resolution of the quantizers is increased from 15 bits to 16.
• Advantage:
  a single scaling factor can be used for all three groups.

## Slide 32: Layer 3 of MPEG-1 Audio
• Main difference:
  Employs a similar filter bank to that used in Layer 2, except using a set of filters with non-equal frequencies.
  Takes into account stereo redundancy.
  Uses Modified Discrete Cosine Transform (MDCT) — addresses problems that the DCT has at boundaries of the window used by overlapping frames by 50%:
  (14.8)

## Slide 33
Fig 14.14: MPEG-Audio Layer 3 Coding.

## Slide 34
Table 14.2 shows various achievable MP3 compression ratios:
Table 14.2: MP3 compression performance

## Slide 35: MPEG-2 AAC (Advanced Audio Coding)
AAC was developed to succeed MP3 for digital audio; delivers better sound quality than MP3 for the same bitrate.
Default audio format for YouTube, iPhone, iTunes, Nintendo, and PlayStation.
The standard vehicle for DVDs:
  Audio coding technology for the DVD-Audio Recordable (DVD-AR) format, also adopted by XM Radio.
Aimed at transparent sound reproduction for theaters.
  Can deliver this at 320 kbps for five channels so that sound can be played from 5 different directions: Left, Right, Center, Left-Surround, and Right-Surround.
  5.1 channel systems also include a low-frequency enhancement (LFE) channel (a “woofer”).
Also capable of delivering high-quality stereo sound at bit-rates below 128 kbps.

## Slide 36: MPEG-2 AAC (Cont’d)
Support up to 48 channels, sampling rates between 8 kHz and 96 kHz, and bit-rates up to 576 kbps per channel.
Like MPEG-1, MPEG-2, supports three different “profiles”, but with a different purpose:
  – Main profile
  – Low Complexity(LC) profile
  – Scalable Sampling Rate (SSR) profile

## Slide 37: MPEG-4 Audio
Integrates several different audio components into one standard: speech compression, perceptually based coders, text-to-speech, and MIDI.
MPEG-4 AAC (Advanced Audio Coding), is similar to the MPEG-2 AAC standard, with some minor changes.
Perceptual Coders
  Incorporate a Perceptual Noise Substitution module.
  Include a Bit-Sliced Arithmetic Coding (BSAC) module.
  Also include a second perceptual audio coder, a vector-quantization method entitled TwinVQ.

## Slide 38: MPEG-4 Audio (Cont’d)
• Structured Coders
  Takes “Synthetic/Natural Hybrid Coding” (SNHC) in order to have very low bit-rate delivery an option.
  Objective: integrate both “natural” multimedia sequences, both video and audio, with those arising synthetically – “structured” audio.
  Takes a “toolbox” approach and allows specification of many such models.
  E.g., Text-To-Speech (TTS) is an ultra-low bit-rate method, and actually works, provided one need not care what the speaker actually sounds like.

## Slide 39: 14.3 Other Audio Codecs
Ogg Vorbis is an open-source audio compression format.
Table 14.3: Comparison of MP3, MPEG-4 AAC, and Ogg Vorbis

## Slide 40: 14.4 MPEG-7 Audio and Beyond
Table 14.4 summarizes the target bitrate ranges and main features of other modern general audio codecs.
Table 14.4: Comparison of audio coding systems

## Slide 41: 14.4 MPEG-7 Audio and Beyond
Difference from current standards:
MPEG-4 is aimed at compression using objects.
MPEG-7 is mainly aimed at “search”: How can we find objects, assuming that multimedia is indeed coded in terms of objects.
  The objective, in terms of audio, is to facilitate the representation and search for sound content, perhaps through the tune or other descriptors.
  An example application supported by MPEG-7 is automatic speech recognition (ASR).
  Further standards in the MPEG sequence are mostly not aimed at further audio compression standardization. For example, MPEG-DASH (Dynamic Adaptive Streaming over HTTP) is aimed at streaming of multimedia.